## Slide 1
🛸 AEROSENSE
Quadcopter 3D Spatial Pollution Mapping System
Dual-Core ESP32-S3 IoT Payload & Live Ground Control Room

## Slide 2
The Core Problem: Fixed Monitoring is Blind
• Fixed Ground Stations: Standard environmental monitors are stationary and only capture air parameters at ground level.
• Temperature Inversion Layers: Warm air bands aloft trap particulates (PM2.5) at higher elevations, which are completely missed by ground sensors.
• Volumetric Gaps: Microclimates and urban topography lead to highly localized 3D pollution pockets.
• Vertical Column Profiling: AeroSense flies a coordinate grid at different altitude layers to create a vertical pollution gradient.
• Hyperlocal Intelligence: Maps 3D spaces in real-time, providing boundary layer data to study trapped emissions.

## Slide 3
Low-Weight, Low-Cost Hardware Stack
• ESP32-S3 DevKit: Dual-core payload processor handling asynchronous queries, sensor data aggregation, and telemetry serialization.
• PMS5003 Sensor: Laser-based particulate counter (PM2.5 & PM10).
• BME280 Module: High-accuracy meteorological reader (Temp, Pressure, Humidity).
• MQ-135 Sensor: Analog sensor for toxic gases (connected via protective resistor divider to ESP32 ADC pin).
• Ra-02 LoRa (433MHz): Long-range, low-bandwidth telemetry transmission.
• Pixhawk Autopilot Integration: Queries GPS position directly via MAVLink (UART), saving weight and sensor cost.
• Budget Efficiency: Built under ₹2,600 total cost (~55% cheaper than legacy Raspberry Pi payloads).

## Slide 4
Embedded Firmware & Optimization
• Dual Firmware Options: MicroPython (asyncio loop for fast iterations) or Arduino C++ (optimized for flight frequency).
• MessagePack Serialization: Packs 13 telemetry fields (coordinates, temperature, pressure, particulates) into a tight 65-byte binary payload.
• Airtime Optimization: Binary serialization slashes LoRa packet transmission times, increasing signal range and drone battery life.
• Real-Time Telemetry Transmission: Direct wireless broadcasting of MessagePack telemetry streams over LoRa or WiFi UDP channels.

## Slide 5
Ground Control Station (GCS) Server
• Multi-Threaded GCS: Runs concurrent receiver threads to ingest data from both LoRa serial radios and WiFi UDP sockets.
• SQLite Persistence: Automatically parses and logs telemetry packages to a local database (aerosense.db) at high frequency.
• Flask REST API: Serves JSON endpoints containing history logs, flight coordinates, and config commands.
• Web Dashboard Hosting: Host and serves React web cockpit files from a single centralized web port.

## Slide 6
Plotly Dash 3D Volumetric Mapping
• 3D Flight Scattering: Dynamic representation of drone flight path in a 3D grid, color-graded by particulate density.
• Spatial Cubic Interpolation: Scipy integration estimates PM2.5 levels at coordinates the drone didn't fly through directly.
• Elevation Slicing: Interactive slider displays 2D horizontal density maps at target altitudes (e.g. 15m, 30m, 50m).
• Real-Time Cockpit Ticker: Displays instant quality alert indicators and system diagnostics feeds.

## Slide 7
AI Forecasting: Inversion Mixing Predictor
• Diurnal Mixing Dynamics: Trapped emissions aloft mix downward to the ground as sunlight breaks the boundary layer.
• Gradient Inputs: Random Forest/XGBoost predictor takes temperature, pressure, and PM2.5 differences between 15m and 50m bands.
• Ground-Level Prediction: Forecasts ground air quality spikes 15–30 minutes in advance with low Mean Absolute Error (MAE).
• Feature Importance: Explains predictions using meteorological gradients as proxies for atmospheric stability.
• Hyperlocal Warning System: Allows GCS to issue public safety warnings before pollutants descend to ground level.

## Slide 8
Mission Planning & Obstacle Safety
• Waypoint Grid Generator: Exports standard ArduPilot mission waypoint files using grid bounds, flight speed, and altitude inputs.
• Obstacle Radar interface: Pre-engineered React cockpit radar designed to display warning notifications (simulated and ready for VL53L1X hardware).
• Remote Config Manager: Directly pulls and overwrites payload settings (warnings, calibration, parameters) over Flask endpoints.